## Slide 1: FortiGate Secure Connectivity & High Availability
DEPI – Egypt Digital Initiative | Fortinet Cybersecurity Engineer Track
Group: R3_DEPI3_ONL3_ISS8_S2
Team: Shahd Yesen Salah Abdelmoamen | Mohamed Ahmed Mohamed Haridy | Merna Medhat Hamdy Rabia | Nada Ahmed Abo-Bakr Abdelnaser | Jana Hany Salah Eldin | Shams Ibrahem Ali Mohamed

## Slide 2: Agenda
Project Overview & Objectives
Network Design (Interfaces, VLANs, Zones)
User Authentication & Groups
SSL‑VPN Configuration
SSL‑VPN Portal & Mapping
Firewall Policies for VPN
IPsec Site‑to‑Site Tunnels
SD‑WAN & Performance SLAs
High Availability (HA Cluster)
Results, Benefits & Future Work

## Slide 3: Project Overview
Organizations need secure remote access, reliable branch communication, and zero‑downtime continuity.
Our solution combines:
  SSL‑VPN for remote users
  IPsec Site‑to‑Site for branch connectivity
  SD‑WAN for intelligent path selection
  HA Active‑Passive for service uptime

## Slide 4: Objectives
Security Goals:
  Encrypt remote and inter‑branch traffic
  Group‑based access control
  Department segmentation (Least Privilege)
Operational Goals:
  Easy onboarding & centralized management
  Automatic failover without interruption

## Slide 5: Network Design
HQ Interfaces, VLANs & Zones

## Slide 6: HQ Interfaces Overview
LAN (port1): 192.168.126.243/24 | Admin: PING/HTTPS/SSH/HTTP
WAN (port3) and port4: External / branch links
port5 & port6: HA heartbeat interfaces
Role separation ensures clarity, security, and continuity.
Notes: Add screenshot: Interfaces page

## Slide 7: VLAN Segmentation
VLAN10: 172.16.10.1/24 (Management)
VLAN20: 172.16.20.1/24 (HR)
VLAN30: 172.16.30.1/24 (IT)
VLAN40: 172.16.40.1/24 (Finance)
VLAN50: 172.16.50.1/24 (Sales)
Each VLAN has independent DHCP range (x.2 – x.254).
Notes: Add screenshot: VLAN list + DHCP ranges

## Slide 8: Zone Design
Zone name: br
Members: VLAN10, VLAN20, VLAN30, VLAN40, VLAN50
Benefits:
  Centralized policies across departments
  Cleaner rules & easy scaling
Notes: Add screenshot: Zone members view

## Slide 9: Access & Connectivity
Users, SSL‑VPN, IPsec

## Slide 10: User Authentication & Groups
Groups created: Guest‑group, SSO_Guest_Users (FSSO), ssl_vpn_users
Users:
  guest → Guest‑group
  vpn_user → ssl_vpn_users
All users are enabled.
Notes: Add screenshots: User Groups & Users tables

## Slide 11: SSL‑VPN Core Settings
SSL‑VPN enabled on LAN (port1)
Listening port: 10443
Server certificate: Fortinet_Factory (to be replaced by trusted CA later)
Idle logout: 3000 sec | Allow access from any host
Client IP pool: SSLVPN_TUNNEL_ADDR1
  10.212.134.200 – 10.212.134.210
Notes: Add screenshot: SSL‑VPN Settings

## Slide 12: SSL‑VPN Portal
Portal name: full‑access
Tunnel mode: Enabled
Split tunneling: Disabled (Full Tunnel)
Source IP pool: SSLVPN_TUNNEL_ADDR1
All client traffic is routed securely through VPN.
Notes: Add screenshot: SSL‑VPN Portal settings

## Slide 13: Portal Mapping
ssl_vpn_users → full‑access
All other users/groups → full‑access
Unified access experience and simplified administration.
Notes: Add screenshot: Authentication/Portal Mapping

## Slide 14: SSL‑VPN Firewall Policy
Policy: ssl.root → LAN(port1)
Source: ssl_vpn_users / ssl_vpn
Destination: LAN
Service: ALL | Schedule: always
Action: ACCEPT | Security profiles: default / deep‑inspection
Notes: Add screenshot: SSL‑VPN policy row

## Slide 15: IPsec Site‑to‑Site Tunnels
Tunnel 1: f1 to f3
  Remote GW: 209.64.2.2 via port4
  IKEv1 Main Mode, PSK authentication
  Phase‑1: DES‑MD5, DES‑SHA1 | DH groups 14, 5
Tunnel 2: f12 to f3
  Remote GW: 209.64.4.2 via port3
  Same crypto + selectors
Notes: Add screenshots: IPsec tunnel edit pages

## Slide 16: Branch / Inter‑VLAN Policies
Core VPN policies (NAT disabled):
  lan_vpn: port2 → vpn (ACCEPT)
  wan_vpn: vpn → port2 (ACCEPT)
Department‑to‑department least‑privilege rules:
  mgmt ↔ mgmt, hr ↔ hr, it ↔ it, fin ↔ fin, sales ↔ sales
Each VLAN reaches only its matching remote subnet.
Notes: Add screenshot: Firewall Policy table

## Slide 17: SD‑WAN
Smart Routing & SLAs

## Slide 18: SD‑WAN Members
SD‑WAN enabled with 2 members:
  vpn
  vpn_tunnel_3
Provides redundant and balanced transport between sites.
Notes: Add screenshot: SD‑WAN zones/members

## Slide 19: SD‑WAN Rules
Default implicit rule:
  Source: all | Destination: all
  Criteria: Source IP | Member: any
Allows dynamic best‑path selection.
Notes: Add screenshot: SD‑WAN Rules list

## Slide 20: Performance SLAs
Health checks configured for:
  Default_DNS (8.8.8.8 / 8.8.4.4)
  FortiGuard, Gmail, Google Search, Office365
Thresholds drive automatic rerouting to best link.
Notes: Add screenshot: Performance SLAs page

## Slide 21: High Availability (HA)
Business Continuity

## Slide 22: HA Active‑Passive Cluster
Mode: Active‑Passive | Priority: 200
Monitored interfaces: port1, port2, port3, port4
Heartbeat: port5, port6 (50/50)
Session pickup enabled for seamless failover.
Notes: Add screenshots: HA cluster settings

## Slide 23: Results & Benefits

## Slide 24: Results
Secure full‑tunnel remote access to HQ via SSL‑VPN
Redundant IPsec tunnels between sites
Smart routing with SD‑WAN + SLAs
Department isolation via VLANs & zone policies
Continuous service ensured by HA

## Slide 25: Benefits
Security: Encrypted links, least‑privilege access, strong segmentation.
Performance & Reliability: SD‑WAN chooses optimal paths, HA prevents downtime.
Scalability: Easy to add VLANs, users, and new branches.

## Slide 26: Challenges & Mitigations
Challenges:
  Matching Phase‑2 selectors across sites
  Aligning policies with VLAN segmentation
  Avoid NAT over IPsec links
Mitigations:
  Standardized naming and configs
  Zone‑based policies
  NAT disabled for S2S traffic

## Slide 27: Future Enhancements
Replace default SSL cert with trusted CA
Enable MFA for VPN users
Add application‑based SD‑WAN rules
Central management via FortiManager
Log analytics via FortiAnalyzer / SIEM

## Slide 28: Conclusion & Q&A
A complete enterprise‑ready FortiGate deployment delivered:
  Remote access ✅
  Branch connectivity ✅
  Smart routing ✅
  High availability ✅
Thank you.